## Slide 1: Background – Capturing the DATA
We need a system in which it is easy to ask questions at the intersection of logic / timing / placement / routing
We cannot be restricted to asking questions only during tool flow
Re-loading the design after construction can be laborious
We want this system to be clean (minimal dependencies required to load data) and to operate well with Python and C++
DD stores all of its data in a single file for convenient management
DD memory/disk footprint is over 10x smaller than the memory consumed by the construction flows
DD load/init times are over 100x faster
DD can load netlist, timing, placement, routing of a one million net design in less than one minute
DD as a solution to solve these problems
Notes: Few people in EDA with working knowledge of logic/timing/placement/wiring APIs.

## Slide 2: Tool Flow Correlation
Density of DD file allows multiple state snapshots
Compare early predictions against later more accurate modeling
Sibling DD files may be linked enabling easy difference analysis
DD
DD
DD
DD
DD
Accuracy
Speed

## Slide 3: Architecture
DD signal
DD tpt
DD Box/Pin/Net
EDA toolset (synthesis, timing, power,noise)
Data import API layer
(C++)
Tool independent
abstraction
layer (C++)
Python Bindings
Read-only
We have done this for
IBM/EDA toolset (IDM, EinsTimer, PDS)
OADD
OpenTimer DD
Analytics Ecosystem
ML using DD
Opportunities for Open-Source Academic/EDA SW collaboration
Core model development