## Slide 1: The Extensible Translating Instruction Set Simulator (ETISS)
Daniel Müller-Gritschneder
Chair of Electronic Design Automation
Technical University of Munich

## Slide 2: Extendable Translating Instruction Set Simulator (ETISS)
So why another ISS?
  Copyleft licenses (GPL) for open-source approaches such as Qemu
    Problem for integration in industrial VPs
  Commercial approaches such as ARM fast models are closed-source.
    Hard to integrate custom functionality or share
ETISS‘s key features:
  ISA-independent Instruction Set Simulator (ISS)
  Fast Dynamic Binary Translation (DBT) based on C as intermediate format
  Easy integration in SystemC/TLM VPs
  Open License Model (TBD: Under consideration is Apache License)
  Advanced plugin-mechanism:
    Easy to integrate new functionality such as tracing/debugging/timing models without „hacking“ the simulation loop

## Slide 3: Processor Models in ETISS
Architecture | ISAs | ISA Peripherals: | Exception Model | Development
OpenRISC OR1K | ORBIS32_I ORBIS32_II ORFPX32 | OR1K Timer OR1K Interrupt Controller GDB Server | Timer Interrupts | Manual (Fixed)
RISC V | RV32I RV32E RV32N Pulpino Extension | Pulpino RISC V Timer, Exception Unit GDB Server | RISC V Pulpino | MDA approach for ISA from nML (Customizable)

## Slide 4: Status
Has been used in TUM’s VPs and works reliably
Advanced features possible - e.g. multi-level simulation principles (Switch the gear!)
Ready to be shared with BSD-3 License (No copy-left)
Planned/Running:
  Get code and documentation ready for open source release (summer ‘19)
  Planned:
    Integration in SW flows (Continuous integration, Unit test environments)
    Lauterbach debug interface support
    Full Pulpino SystemC VP
    Linux VP

## Slide 5: BACKUP – For Distribution

## Slide 6: ETISS Simulation Loop
Translate Block
Fetch Block
Compile and Cache Block
Block Cached?
Lookup Block
In Translation Cache
Execute Block and Load/Store Accesses
CPU Exception?
Handle CPU Exception
Handle System Exception
Translation Plugin
JITImpl
ArchImpl
or1k
(RISC-V)
CoRoutinePlugin
InterruptListener
Plugin
SystemWrapper Plugin
Determine next block
System Exception?
Determine start block
yes
no
yes
no
yes
RegisterDevice Plugin

## Slide 7: Translation
Translate Block
Decode Instruction
Generate C-code snippet for each instruction in block
Append all C-code snippets into C-function for complete block
Compile C-function of block into shared library for simulation host
Blocks are cached to avoid re-translation
(…)
case 4:
{
cpu->cpuTime_ps += cpu->cpuCycleTime_ps;
(((OR1K*)cpu)->R[ 4 ]) = (((OR1K*)cpu)->R[ 3 ])& 2;
}
(…)
0xA1 00 02 C4
ANDI R4,R3,#2
Decode
Translate
Compile
Block_X.so

## Slide 8: ETISS Performance (OR1K Architecture)
Target SW | #Instr | Plugins | Mode | JIT | Perf.[MIPS] | Sim. Time [s]
edge | 30E3 | Logger | Stand-alone | TCC | 1,39 | 0.22
 |  |  |  | GCC | 1,19 | 0.25
 |  |  |  | LLVM | 0.27 | 1.1
isort | 2.8E6 |  |  | TCC | 13,60 | 0.22
 |  |  |  | GCC | 11,90 | 0.24
 |  |  |  | LLVM | 3,45 | 0.83
PI control | 2.0E9 | Timer, PIC, Reset Module | SystemC | TCC | 49.5 | 40.4
 |  |  |  | GCC | 54.7 | 36.5
 |  |  |  | LLVM | 59.9 | 33.3
Robotic Arm | 7.3E9 | Timer, PIC, Reset Module | SystemC | LLVM | 14,1 | 505
 |  |  | SystemC with DMI | LLVM | 22,1 | 333
DMI: Direct Memory Interface

## Slide 9: Plugin Types
TranslationPlugin:
  Called when new block is translated.
  Can add more translation code, e.g. instruction counter, tracing, timing models
CoRoutinePlugin:
  Called before new block is executed.
  Can react on external events e.g., interrupts, user input , faulit injection trigger, etc.
SystemWrapperPlugin:
  Called before accesses memory.
  Can be used to model memory-mapped devices
InterruptListenerPlugin:
  Called when interrupt is received.
RegisterListenerPlugin:
  Notification when CPU registers are updated.
  Can be used to model devices that are controlled by special-purpose registers of the processor.
ISA Plugin ArchImpl:
  Used to model processor ISA and architecture.
  Atm support for or1k, RISC-V, ARM M0
JIT Plugin:
  Compiler plugin to translate C to host machine.
  Atm support for LLVM, gcc, and tcc (Tested on Ubuntu 14 and Ubuntu16)